汽车刹车油检测仪

AUTOMOTIVE BRAKE FLUID TESTER

DY23

操作说明:

1 . 打开主机背面的电池,将1节9V电池按正负标识放入电池仓内。

2 . 装入电池后,按POWER按钮开机，所有指示灯闪亮一次,蜂鸣响两秒，表明产品自检成功。

3 . 按下SELECT按钮,选择DOT3,DOT4,DOT5 .1类型刹车油,且有状态指示灯指示。

5 . 将测试探头插入刹车油中,(注:如果进行重复测试需将探头擦拭干净,否则会影响测试效果。)

红黄绿灯的含义如下：

绿灯表示刹车油含水量小于1%

第一个黄灯表示刹车油含水量大约1. 5%左右

第二个黄灯表示刹车油含水量大约2. 5%左右	含水量LED指示灯

(water content indicator)

第一个红灯表示含水量大约3%左右第二个红灯表示含水量大于4%

6 . 按POWER按钮，指示灯将熄灭后关机。

DOT3,DOT4,D0T5 . 1

指示灯（indictor）

建议：

1 . 每次测试完毕后，请将探头拭擦干净，避免存留的污迹影响下次使用。

2 . 长时间不使用，建议取出电池，将产品放置于常温干燥处保存。

| 电源开 |  |
| --- | --- |
| 关按钮 |  |
| （POWER | 刹车油类型选择按钮 |
| button） | （SELECT button） |

测试探针

( test probe)

Operation Manual:

- Install one 9V(6F22) battery at the back of tester.

- After inserting the battery, press POWER button to turn on the tester, all LEDs lights turn on with buzzer sounding, indicates the product self-test is successful.

- Press SELECT button, it will locate DOT3 model automatically.

- Each time you push the SELECT button, it will recycle from DOT3 to DOT4 to DOT5.1 with the indicator LEDs.

- Immerse the probe into brake fluid, the different colored LED lights mean as below:

Green Light: indicates the brake fluid water content is below 1%

The First Yellow Light: indicates the brake fluid water content is approximately 1.5%

The Second Yellow Light: indicates the brake fluid water content is approximately 2.5%

The First Red Light: indicates the brake fluid water content is approximately 3%

The Second Red Light: indicates the brake fluid water content is more than 4% 6. Press POWER button to turn off the tester.

Note:

- After use, please clean the probe and avoid any retention of stains that might affect the test.

- If in use for a long time, best to remove all batteries and store in a dry place at normal room temperature.